## Slide 1: CovMo NT
GT Internal Training
2016 Nov

## Slide 2: Question
Why we need NT data
What’s NT ?
What propose we using NT in CovMo
How important for correct NT data ?
Which module need NT data?

## Slide 4: NT Process Steps
確認csv是否完整
若不完整拿上 版的補
完成ntdb後會給event parser 用
為了要把編碼的資料解碼
每個基站之間的分布 距離關係 可以知道密度
不同project供的資料

## Slide 5: GT NT Definition document
Schema of Product
  \\ghtdb02\project3\CovMo\CovMo_NT
Schema and definition
  \\ghtdb02\project3\
  FET, Etisalat, Vittel, STC, …
  \\ghtdb02\project3\SingTel\NT

## Slide 6: CovMo Input Data Source
Item | Data Type | Data Source | 
1 | Trace Data | GPEH, CTR, CTUM, PCHR/MR, UCHR, MME, CHR, eNB (eNodeB) maxdepth trace | 
2 | Network Topology (SITE DB) | Cell/Site Planning Data/ MNIS/SIMS/ | 
3 | Configuration Management Data (CM) | Eric OSS- .xml Huawei U2000-CFGMML.txt | 
4 | Antenna Info |  | 
\\ghtdb02\project3\SingTel\NT\Data\NT_Source\SITE DATA\SIMS data ample.xlsx
2+3形成NT file

## Slide 7: NT Source File
Huawei
Ericsson
ALU
Nokia (NSN) File location: /data/nt_export

## Slide 8: NT Process Steps

## Slide 9: NT Process Step 1.
DP will collect all SIMS/SITEDB/MNIS (vendor NT csv/excel file) and CM file into our Server, General in AP server :
  NT source folder structure
  /data/nt_export/source/Date/cm
  /data/nt_export/source/Date/nt
  /opt/covmo/parser/nt/output/antenna (for NT_ANTENNA …. Some columns will reference from this ANTENNA_INFO.csv)
OPTUS
Etisalat

## Slide 10: NT Process Step 2.
DP Call NT Parser for process those vendor’s data
  V3_Antenna_Info_Parser.py
  V3_Antenna_Profile_Parser.py
  V3_Empth_Header.py
  V3_Ericsson_CM_Parser_GSM.py
  V3_Ericsson_CM_Parser_LTE.py
  V3_Ericsson_CM_Parser_UMTS.py
  V3_Huawei_CM_Parser_GSM.py
  V3_Huawei_CM_Parser_LTE.py
  V3_Huawei_CM_Parser_UMTS.py
  …. Etc
/opt/covmo/parser/nt/

## Slide 11: NT Process Step 3.
Parser will ouput each (vendor/Tech) parser’s output into /opt/covmo/parser/nt/output/[YYYYMMDD]

## Slide 12: NT Process Step 4.
DP will copy those folder (without failed log) into /opt/covmo/parser/nt/nt_ready

## Slide 13: NT Process Output CSVs
LTE | UMTS | GSM
(NT_PU.CSV) NT_CELL_LTE.CSV NT_ANTENNA_LTE.CSV NT_NBR_4_2_LTE.CSV NT_NBR_4_3_LTE.CSV NT_NBR_4_4_LTE.CSV NT_MME_LTE.CSV NT_TAC_CELL_LTE.CSV | NT_RNC.CSV NT_CELL.CSV NT_ANTENNA.CSV NT_NEIGHBOR.CSV NT_CELL_ATTRIBUTE.CSV | NT_BSC.CSV NT_CELL_GSM.CSV NT_ANTENNA_GSM.CSV NT_NEIGHBOR_GSM.CSV
Cell
Nbr 同一個system的table, 不同
Antenna 定位

## Slide 14: NT Process Step 5
After nt_ready (ready files)
AP 1 (and 2) will start using /opt/covmo/parser/nt/nt_ready  copy to their won /opt/covmo/parser/nt/output/20160512
using /opt/covmo/parser/nt/output/20160512 to generate gt_nt_20160512 NT DB
AP:application server

## Slide 15: NT Process Step 6 ( To be change )
Create NT DB
  Create NT DB Schema (SP)
  Load NT csv into NTDB
  Generate Voronoi
  NT checking & update & dump records (from SP)
  if step 6 success, will backup db file into /opt/covmo/parser/nt/db_ready,
  if step 5 fail, will using last /opt/covmo/parser/nt/db_ready

## Slide 16: NT Process Step 7 ( To be change )
Gateway server cron job will copy /opt/covmo/parser/nt/db_ready from AP1 to them
Gateway server cron job @ closed time of 1, another cron job will copy /opt/covmo/parser/nt/nt_ready
Gateway server cron job will using db_ready for gt_nt_20160512 (new date NT DB )

## Slide 17: Addition: Process ANTENNA_INFO
Antenna Profile
Antenna Atoll format
Antenna Info GT format \\Internal1\temp\training\Internal\
\\GHTDB02\Project3\CovMo\CovMo_NT\ANTENNA

## Slide 18: ANTENNA_INFO
What need to know
  Antenna Model
  Antenna Type (Omni/Sector)
  Antenna Gain
  Antenna BeamWidth
    dB3
    dB6
  Azimuth
  Pattern

## Slide 19: Antenna Model
Propagation Model for the signal strength (Gain loss)

## Slide 20: Antenna Pattern - Horizontal

## Slide 21: Antenna Pattern - Vertical

## Slide 22: ANTENNA_INFO
\\internal1\temp\Candy\NT\ANTENNA_INFO.csv

## Slide 23: Thank you! Questions & Comments
23
Notes: 23
in conclusion, CovMo supports you to have
Better network quality.
Better intelligence regarding how to improve network to recover most revenue
More precise femtocell deployment.
Less unnecessary micro cells.
And CovMo will be the key for your improving coverage, capacity, and /quality of the network.

## Slide 25: File link
Antenna Info
  \\internal1\temp\Candy\NT\ANTENNA_INFO.csv
  Antenna Profile \\internal1\temp\Candy\NT\Antenna_Library\download_antenna
NT Rule definition
  SIMS \\ghtdb02\project3\SingTel\NT\Data\NT_Source\SITE DATA\SIMS data ample.xlsx
  NT Rule \\ghtdb02\project3\SingTel\NT\CovMo_NT_Rule_20160217.xlsx
  CM \\ghtdb02\project3\SingTel\NT\Data\NT_Source\cm

## Slide 26
Advance ….